Tools & supplies

1 1/16 6-point socket

Adapter, ¾” male hose to valve stem “Blow Out Plug”

Air compressor with regulator set to 40psi max

4 gallons anti-freeze

Winterizing Montana

- Drain holding tanks, leave valves open

- Drain water tank

- Drain portable water filter, let filters dry

- Turn “Water Heater Bypass” to the “on” position (horizontal)

- Remove water heater drain/anode 1 1/16” socket, leave out

- Connect the air line to the “Black Tank Flush Valve”, blow out black tank flush

- Connect air line to “City Water Connection”; Blow water out of lines with air (40psi max), open each faucet cold & hot,  in turn

  - Turn the “Fresh Water Tank Power Fill Valve” to the “Fill” position (vertical)

    - Blow water out of the line going to the fresh water tank

    - Turn the “Fresh Water Tank Power Fill Valve” to the “Normal Flow” position (horizontal)

  - Outside faucet, cold, hot

  - Kitchen sink, cold, hot

  - Bath sink, cold, hot

  - Shower, cold, hot

  - Washer, cold, hot

  - Toilet

  - Toilet sprayer

- Open faucets

- Open low point drains, allow to drain

- Close faucets

- Close low point drains

- Close holding tank valves

- Close water tank drain

- Connect a short hose to the “Freeze Guard” connection, other end into a container of RV antifreeze

- Turn the winterizing valve to the “on” position (horizontal)

- Turn on water pump, monitor antifreeze container to keep hose submerged. Open each faucet cold then hot, in turn until antifreeze flows (may have to use portable water pump to provide the anti freeze under pressure)

  - Kitchen sink, cold, hot

  - Bath sink, cold, hot

  - Shower, cold, hot

  - Washer, cold, hot

  - Toilet

  - Toilet sprayer

  - Low points

- Make sure antifreeze fills each sink trap

- Shut pump off

- Close faucets

- Open low point drains, verify antifreeze is present

- Close low point drains

- Wipe anti-freeze out of sinks

- Sta-Bil generators, chain saw, etc.

- Put anti-mouse dryer sheets in trailer

- Remove tire pressure monitors

De-Winterizing Montana

- Use clean-out spout to flush out water heater tank

- Connect a short hose to the “Freeze Guard” connection, other end into a container of clean fresh water

- Winterizing valve should still be in the “on” position (horizontal)

- Turn on water pump and pump several gallons through any faucet to clean out water pump

- Turn winterizing valve to the “off” position (vertical)

- Hook garden hose to city water with regulator, turn on

- Open low point drains, run until clear, close low point drains

- Begin running water through all faucets, cold & hot, until clear, run for 1 hour or more

- Install water heater drain/anode, use Teflon tape

- Turn “Water Heater Bypass” to the “off” position (vertical)

- Fill water heater, run some water through it

- Install new water filter

- Sanitize fresh water tank

- Fill fresh water tank

- Check tire pressures

- Install tire pressure monitors

- Change generator oil

- Prep Generators

- CO detector and smoke detector batteries

- Outside thermometer battery

- Grease suspension